## Slide 1: Chapter 8: State Machine and Concurrent Process Model

## Slide 2: Outline
Models vs. Languages
State Machine Model
  FSM/FSMD
  HCFSM and Statecharts Language
  Program-State Machine (PSM) Model
Concurrent Process Model
  Communication
  Synchronization
  Implementation
Dataflow Model
Real-Time Systems

## Slide 3: Introduction
Describing embedded system’s processing behavior
  Can be extremely difficult
    Complexity increasing with increasing IC capacity
      Past: washing machines, small games, etc.
        Hundreds of lines of code
      Today: TV set-top boxes, Cell phone, etc.
        Hundreds of thousands of lines of code
    Desired behavior often not fully understood in beginning
      Many implementation bugs due to description mistakes/omissions
  English (or other natural language) common starting point
    Precise description difficult to impossible
    Example: Motor Vehicle Code – thousands of pages long...

## Slide 4: An example of trying to be precise in English
California Vehicle Code
  Right-of-way of crosswalks
    21950. (a) The driver of a vehicle shall yield the right-of-way to a pedestrian crossing the roadway within any marked crosswalk or within any unmarked crosswalk at an intersection, except as otherwise provided in this chapter.
    (b) The provisions of this section shall not relieve a pedestrian from the duty of using due care for his or her safety. No pedestrian shall suddenly leave a curb or other place of safety and walk or run into the path of a vehicle which is so close as to constitute an immediate hazard. No pedestrian shall unnecessarily stop or delay traffic while in a marked or unmarked crosswalk.
    (c) The provisions of subdivision (b) shall not relieve a driver of a vehicle from the duty of exercising due care for the safety of any pedestrian within any marked crosswalk or within any unmarked crosswalk at an intersection.
  All that just for crossing the street (and there’s much more)!

## Slide 5: Models and languages
How can we (precisely) capture behavior?
  We may think of languages (C, C++), but computation model is the key
Common computation models:
  Sequential program model
    Statements, rules for composing statements, semantics for executing them
  Communicating process model
    Multiple sequential programs running concurrently
  State machine model
    For control dominated systems, monitors control inputs, sets control outputs
  Dataflow model
    For data dominated systems, transforms input data streams into output streams
  Object-oriented model
    For breaking complex software into simpler, well-defined pieces

## Slide 6: Models vs. languages
Computation models describe system behavior
  Conceptual notion, e.g., recipe, sequential program
Languages capture models
  Concrete form, e.g., English, C
Variety of languages can capture one model
  E.g., sequential program model  C,C++, Java
One language can capture variety of models
  E.g., C++ → sequential program model, object-oriented model, state machine model
Certain languages better at capturing certain computation models
Models
Languages
Recipe
Spanish
English
Japanese
Poetry
Story
Sequent.
program
C++
C
Java
State
machine
Data-
flow
Recipes vs. English
Sequential programs vs. C

## Slide 7: Text versus Graphics
Models versus languages not to be confused with text versus graphics
  Text and graphics are just two types of languages
    Text: letters, numbers
    Graphics: circles, arrows (plus some letters, numbers)
X = 1;
Y = X + 1;
X = 1
Y = X + 1

## Slide 8: Introductory example: An elevator controller
Simple elevator controller
  Request Resolver resolves various floor requests into single requested floor
  Unit Control moves elevator to this requested floor
Try capturing in C...
“Move the elevator either up or down to reach the requested floor. Once at the requested floor, open the door for at least 10 seconds, and keep it open until the requested floor changes. Ensure the door is never open while moving. Don’t change directions unless there are no higher requests when moving up or no lower requests when moving down…”
Partial English description
buttons
inside
elevator
Unit
Control
b1
down
open
floor
...
Request
Resolver
...
up/down
buttons on each
floor
b2
bN
up1
up2
dn2
dnN
req
up
System interface
up3
dn3

## Slide 9: Elevator controller using a sequential program model
“Move the elevator either up or down to reach the requested floor. Once at the requested floor, open the door for at least 10 seconds, and keep it open until the requested floor changes. Ensure the door is never open while moving. Don’t change directions unless there are no higher requests when moving up or no lower requests when moving down…”
Partial English description
buttons
inside
elevator
Unit
Control
b1
down
open
floor
...
Request
Resolver
...
up/down
buttons on each
floor
b2
bN
up1
up2
dn2
dnN
req
up
System interface
up3
dn3
Sequential program model
void UnitControl()
{
up = down = 0; open = 1;
while (1) {
while (req == floor);
open = 0;
if (req > floor) { up = 1;}
else {down = 1;}
while (req != floor);
up = down = 0;
open = 1;
delay(10);
}
}
void RequestResolver()
{
while (1)
...
req = ...
...
}
void main()
{
Call concurrently:
UnitControl() and
RequestResolver()
}
Inputs: int floor; bit b1..bN; up1..upN-1; dn2..dnN;
Outputs: bit up, down, open;
Global variables: int req;
You might have come up with something having even more if statements.

## Slide 10: Finite-state machine (FSM) model
Trying to capture this behavior as sequential program is a bit awkward
Instead, we might consider an FSM model, describing the system as:
  Possible states
    E.g., Idle, GoingUp, GoingDn, DoorOpen
  Possible transitions from one state to another based on input
    E.g., req > floor
  Actions that occur in each state
    E.g., In the GoingUp state, u,d,o,t = 1,0,0,0 (up = 1, down, open, and timer_start = 0)
Try it...

## Slide 11: Finite-state machine (FSM) model
Idle
GoingUp
req > floor
req < floor
!(req > floor)
!(timer < 10)
req < floor
DoorOpen
GoingDn
req > floor
u,d,o, t = 1,0,0,0
u,d,o,t = 0,0,1,0
u,d,o,t = 0,1,0,0
u,d,o,t = 0,0,1,1
u is up, d is down, o is open
req == floor
!(req<floor)
timer < 10
t is timer_start
UnitControl process using a state machine

## Slide 12: Formal definition
An FSM is a 6-tuple F<S, I, O, F, H, s0>
  S is a set of all states {s0, s1, …, sl}
  I is a set of inputs {i0, i1, …, im}
  O is a set of outputs {o0, o1, …, on}
  F is a next-state function (S x I → S)
  H is an output function (S → O)
  s0 is an initial state
Moore-type
  Associates outputs with states (as given above, H maps S → O)
Mealy-type
  Associates outputs with transitions (H maps S x I → O)
Shorthand notations to simplify descriptions
  Implicitly assign 0 to all unassigned outputs in a state
  Implicitly AND every transition condition with clock edge (FSM is synchronous)

## Slide 13: Finite-state machine with datapath model (FSMD)
FSMD extends FSM: complex data types and variables for storing data
  FSMs use only Boolean data types and operations, no variables
FSMD: 7-tuple <S, I , O, V, F, H, s0>
  S is a set of states {s0, s1, …, sl}
  I is a set of inputs {i0, i1, …, im}
  O is a set of outputs {o0, o1, …, on}
  V is a set of variables {v0, v1, …, vn}
  F is a next-state function (S x I x V → S)
  H is an action function (S → O + V)
  s0 is an initial state
I,O,V may represent complex data types (i.e., integers, floating point, etc.)
F,H may include arithmetic operations
H is an action function, not just an output function
  Describes variable updates as well as outputs
Complete system state now consists of current state, si, and values of all variables
Idle
GoingUp
req > floor
req < floor
!(req > floor)
!(timer < 10)
req < floor
DoorOpen
GoingDn
req > floor
u,d,o, t = 1,0,0,0
u,d,o,t = 0,0,1,0
u,d,o,t = 0,1,0,0
u,d,o,t = 0,0,1,1
u is up, d is down, o is open
req == floor
!(req<floor)
timer < 10
t is timer_start
We described UnitControl as an FSMD

## Slide 14: Describing a system as a state machine
  1. List all possible states
  2. Declare all variables (none in this example)
  3. For each state, list possible transitions, with conditions, to other states
  4. For each state and/or transition, list associated actions
  5. For each state, ensure exclusive and complete exiting transition conditions
    No two exiting conditions can be true at same time
      Otherwise nondeterministic state machine
    One condition must be true at any given time
      Reducing explicit transitions should be avoided when first learning
req > floor
!(req > floor)
u,d,o, t = 1,0,0,0
u,d,o,t = 0,0,1,0
u,d,o,t = 0,1,0,0
u,d,o,t = 0,0,1,1
u is up, d is down, o is open
req < floor
req > floor
req == floor
req < floor
!(req<floor)
!(timer < 10)
timer < 10
t is timer_start
Idle
GoingUp
DoorOpen
GoingDn

## Slide 15: State machine vs. sequential program model
Different thought process used with each model
State machine:
  Encourages designer to think of all possible states and transitions among states based on all possible input conditions
Sequential program model:
  Designed to transform data through series of instructions that may be iterated and conditionally executed
State machine description excels in many cases
  More natural means of computing in those cases
  Not due to graphical representation (state diagram)
    Would still have same benefits if textual language used (i.e., state table)
    Besides, sequential program model could use graphical representation (i.e., flowchart)

## Slide 16: Try Capturing Other Behaviors with an FSM
E.g., Answering machine blinking light when there are messages
E.g., A simple telephone answering machine that answers after 4 rings when activated
E.g., A simple crosswalk traffic control light
Others

## Slide 17: Capturing state machines in sequential programming language
Despite benefits of state machine model, most popular development tools use sequential programming language
  C, C++, Java, Ada, VHDL, Verilog, etc.
  Development tools are complex and expensive, therefore not easy to adapt or replace
    Must protect investment
Two approaches to capturing state machine model with sequential programming language
  Front-end tool approach
    Additional tool installed to support state machine language
      Graphical and/or textual state machine languages
      May support graphical simulation
      Automatically generate code in sequential programming language that is input to main development tool
    Drawback: must support additional tool (licensing costs, upgrades, training, etc.)
  Language subset approach
    Most common approach...

## Slide 18: Language subset approach
Follow rules (template) for capturing state machine constructs in equivalent sequential language constructs
Used with software (e.g.,C) and hardware languages (e.g.,VHDL)
Capturing UnitControl state machine in C
  Enumerate all states (#define)
  Declare state variable initialized to initial state (IDLE)
  Single switch statement branches to current state’s case
  Each case has actions
    up, down, open, timer_start
  Each case checks transition conditions to determine next state
    if(…) {state = …;}
#define IDLE0
#define GOINGUP1
#define GOINGDN2
#define DOOROPEN3
void UnitControl() {
int state = IDLE;
while (1) {
switch (state) {
IDLE: up=0; down=0; open=1; timer_start=0;
if (req==floor) {state = IDLE;}
if (req > floor) {state = GOINGUP;}
if (req < floor) {state = GOINGDN;}
break;
GOINGUP: up=1; down=0; open=0; timer_start=0;
if (req > floor) {state = GOINGUP;}
if (!(req>floor)) {state = DOOROPEN;}
break;
GOINGDN: up=1; down=0; open=0; timer_start=0;
if (req < floor) {state = GOINGDN;}
if (!(req<floor)) {state = DOOROPEN;}
break;
DOOROPEN: up=0; down=0; open=1; timer_start=1;
if (timer < 10) {state = DOOROPEN;}
if (!(timer<10)){state = IDLE;}
break;
}
}
}
UnitControl state machine in sequential programming language

## Slide 19: General template
#define S0 0
#define S1 1
...
#define SN N
void StateMachine() {
int state = S0; // or whatever is the initial state.
while (1) {
switch (state) {
S0:
// Insert S0’s actions here & Insert transitions Ti leaving S0:
if( T0’s condition is true ) {state = T0’s next state; /*actions*/ }
if( T1’s condition is true ) {state = T1’s next state; /*actions*/ }
...
if( Tm’s condition is true ) {state = Tm’s next state; /*actions*/ }
break;
S1:
// Insert S1’s actions here
// Insert transitions Ti leaving S1
break;
...
SN:
// Insert SN’s actions here
// Insert transitions Ti leaving SN
break;
}
}
}

## Slide 20: HCFSM and the Statecharts language
Hierarchical/concurrent state machine model (HCFSM)
  Extension to state machine model to support hierarchy and concurrency
  States can be decomposed into another state machine
    With hierarchy has identical functionality as Without hierarchy, but has one less transition (z)
    Known as OR-decomposition
  States can execute concurrently
    Known as AND-decomposition
Statecharts
  Graphical language to capture HCFSM
  timeout: transition with time limit as condition
  history: remember last substate OR-decomposed state A was in before transitioning to another state B
    Return to saved substate of A when returning from B instead of initial state
A1
z
B
A2
z
x
y
w
Without hierarchy
A1
z
B
A2
x
y
A
w
With hierarchy
C1
C2
x
y
C
B
D1
D2
u
v
D
Concurrency

## Slide 21: UnitControl with FireMode
FireMode
  When fire is true, move elevator to 1st floor and open door
Without hierarchy
Idle
GoingUp
req>floor
req<floor
!(req>floor)
timeout(10)
req<floor
DoorOpen
GoingDn
req>floor
u,d,o = 1,0,0
u,d,o = 0,0,1
u,d,o = 0,1,0
req==floor
!(req<floor)
fire
fire
fire
fire
FireGoingDn
floor>1
u,d,o = 0,1,0
u,d,o = 0,0,1
!fire
FireDrOpen
floor==1
fire
u,d,o = 0,0,1
UnitControl
fire
!fire
FireGoingDn
floor>1
u,d,o = 0,1,0
FireDrOpen
floor==1
fire
FireMode
u,d,o = 0,0,1
With hierarchy
Idle
GoingUp
req>floor
req<floor
!(req>floor)
timeout(10)
req<floor
DoorOpen
GoingDn
req>floor
u,d,o = 1,0,0
u,d,o = 0,0,1
u,d,o = 0,1,0
req==floor
!(req>floor)
u,d,o = 0,0,1
NormalMode
UnitControl
NormalMode
FireMode
fire
!fire
UnitControl
ElevatorController
RequestResolver
...
With concurrent RequestResolver
  w/o hierarchy: Getting messy!
  w/ hierarchy: Simple!

## Slide 22: Program-state machine model (PSM): HCFSM plus sequential program model
Program-state’s actions can be FSM or sequential program
  Designer can choose most appropriate
Stricter hierarchy than HCFSM used in Statecharts
  transition between sibling states only, single entry
  Program-state may “complete”
    Reaches end of sequential program code, OR
    FSM transition to special complete substate
    PSM has 2 types of transitions
      Transition-immediately (TI): taken regardless of source program-state
      Transition-on-completion (TOC): taken only if condition is true AND source program-state is complete
  SpecCharts: extension of VHDL to capture PSM model
  SpecC: extension of C to capture PSM model
up = down = 0; open = 1;
while (1) {
while (req == floor);
open = 0;
if (req > floor) { up = 1;}
else {down = 1;}
while (req != floor);
open = 1;
delay(10);
}
}
NormalMode
FireMode
up = 0; down = 1; open = 0;
while (floor > 1);
up = 0; down = 0; open = 1;
fire
!fire
UnitControl
ElevatorController
RequestResolver
...
req = ...
...
int req;
NormalMode and FireMode described as sequential programs
Black square originating within FireMode indicates !fire is a TOC transition
  Transition from FireMode to NormalMode only after FireMode completed

## Slide 23: Role of appropriate model and language
Finding appropriate model to capture embedded system is an important step
  Model shapes the way we think of the system
    Originally thought of sequence of actions, wrote sequential program
      First wait for requested floor to differ from target floor
      Then, we close the door
      Then, we move up or down to the desired floor
      Then, we open the door
      Then, we repeat this sequence
    To create state machine, we thought in terms of states and transitions among states
      When system must react to changing inputs, state machine might be best model
        HCFSM described FireMode easily, clearly
Language should capture model easily
  Ideally should have features that directly capture constructs of model
  FireMode would be very complex in sequential program
    Checks inserted throughout code
  Other factors may force choice of different model
    Structured techniques can be used instead
      E.g., Template for state machine capture in sequential program language

## Slide 24: Concurrent process model
Describes functionality of system in terms of two or more concurrently executing subtasks
Many systems easier to describe with concurrent process model because inherently multitasking
E.g., simple example:
  Read two numbers X and Y
  Display “Hello world.” every X seconds
  Display “How are you?” every Y seconds
More effort would be required with sequential program or state machine model
Subroutine execution over time
time
ReadX
ReadY
PrintHelloWorld
PrintHowAreYou
Simple concurrent process example
ConcurrentProcessExample() {
x = ReadX()
y = ReadY()
Call concurrently:
PrintHelloWorld(x) and
PrintHowAreYou(y)
}
PrintHelloWorld(x) {
while( 1 ) {
print "Hello world."
delay(x);
}
}
PrintHowAreYou(x) {
while( 1 ) {
print "How are you?"
delay(y);
}
}
Sample input and output
Enter X: 1
Enter Y: 2
Hello world. (Time = 1 s)
Hello world. (Time = 2 s)
How are you? (Time = 2 s)
Hello world. (Time = 3 s)
How are you? (Time = 4 s)
Hello world. (Time = 4 s)
...

## Slide 25: Dataflow model
Derivative of concurrent process model
Nodes represent transformations
  May execute concurrently
Edges represent flow of tokens (data) from one node to another
  May or may not have token at any given time
When all of node’s input edges have at least one token, node may fire
When node fires, it consumes input tokens processes transformation and generates output token
Nodes may fire simultaneously
Several commercial tools support graphical languages for capture of dataflow model
  Can automatically translate to concurrent process model for implementation
  Each node becomes a process
modulate
convolve
transform
A
B
C
D
Z
Nodes with more complex transformations
t1
t2
+
–
*
A
B
C
D
Z
Nodes with arithmetic transformations
t1
t2
Z = (A + B) * (C - D)

## Slide 26: Synchronous dataflow
With digital signal-processors (DSPs), data flows at fixed rate
Multiple tokens consumed and produced per firing
Synchronous dataflow model takes advantage of this
  Each edge labeled with number of tokens consumed/produced each firing
  Can statically schedule nodes, so can easily use sequential program model
    Don’t need real-time operating system and its overhead
How would you map this model to a sequential programming language? Try it...
Algorithms developed for scheduling nodes into “single-appearance” schedules
  Only one statement needed to call each node’s associated procedure
    Allows procedure inlining without code explosion, thus reducing overhead even more
modulate
convolve
transform
A
B
C
D
Z
Synchronous dataflow
mt1
ct2
mA
mB
mC
mD
tZ
tt1
tt2
t1
t2

## Slide 27: Concurrent processes and real-time systems

## Slide 28: Concurrent processes
Consider two examples having separate tasks running independently but sharing data
Difficult to write system using sequential program model
Concurrent process model easier
  Separate sequential programs (processes) for each task
  Programs communicate with each other
Heartbeat Monitoring System
B[1..4]
Heart-beat pulse
Task 1:
Read pulse
If pulse < Lo then
Activate Siren
If pulse > Hi then
Activate Siren
Sleep 1 second
Repeat
Task 2:
If B1/B2 pressed then
Lo = Lo +/– 1
If B3/B4 pressed then
Hi = Hi +/– 1
Sleep 500 ms
Repeat
Set-top Box
Input Signal
Task 1:
Read Signal
Separate Audio/Video
Send Audio to Task 2
Send Video to Task 3
Repeat
Task 2:
Wait on Task 1
Decode/output Audio
Repeat
Task 3:
Wait on Task 1
Decode/output Video
Repeat
Video
Audio

## Slide 29: Process
A sequential program, typically an infinite loop
  Executes concurrently with other processes
  We are about to enter the world of “concurrent programming”
Basic operations on processes
  Create and terminate
    Create is like a procedure call but caller doesn’t wait
      Created process can itself create new processes
    Terminate kills a process, destroying all data
    In HelloWord/HowAreYou example, we only created processes
  Suspend and resume
    Suspend puts a process on hold, saving state for later execution
    Resume starts the process again where it left off
  Join
    A process suspends until a particular child process finishes execution

## Slide 30: Communication among processes
Processes need to communicate data and signals to solve their computation problem
  Processes that don’t communicate are just independent programs solving separate problems
Basic example: producer/consumer
  Process A produces data items, Process B consumes them
  E.g., A decodes video packets, B display decoded packets on a screen
How do we achieve this communication?
  Two basic methods
    Shared memory
    Message passing
processA() {
// Decode packet
// Communicate packet to B
}
}
void processB() {
// Get packet from A
// Display packet
}
Encoded video packets
Decoded video packets
To display

## Slide 31: Shared Memory
Processes read and write shared variables
  No time overhead, easy to implement
  But, hard to use – mistakes are common
Example: Producer/consumer with a mistake
  Share buffer[N], count
    count = # of valid data items in buffer
  processA produces data items and stores in buffer
    If buffer is full, must wait
  processB consumes data items from buffer
    If buffer is empty, must wait
  Error when both processes try to update count concurrently (lines 10 and 19) and the following execution sequence occurs. Say “count” is 3.
    A loads count (count = 3) from memory into register R1 (R1 = 3)
    A increments R1 (R1 = 4)
    B loads count (count = 3) from memory into register R2 (R2 = 3)
    B decrements R2 (R2 = 2)
    A stores R1 back to count in memory (count = 4)
    B stores R2 back to count in memory (count = 2)
  count now has incorrect value of 2
01: data_type buffer[N];
02: int count = 0;
03: void processA() {
04: int i;
05: while( 1 ) {
06: produce(&data);
07: while( count == N );/*loop*/
08: buffer[i] = data;
09: i = (i + 1) % N;
10: count = count + 1;
11: }
12: }
13: void processB() {
14: int i;
15: while( 1 ) {
16: while( count == 0 );/*loop*/
17: data = buffer[i];
18: i = (i + 1) % N;
19: count = count - 1;
20: consume(&data);
21: }
22: }
23: void main() {
24: create_process(processA);
25: create_process(processB);
26: }

## Slide 32: Message Passing
Message passing
  Data explicitly sent from one process to another
    Sending process performs special operation, send
    Receiving process must perform special operation, receive, to receive the data
    Both operations must explicitly specify which process it is sending to or receiving from
    Receive is blocking, send may or may not be blocking
  Safer model, but less flexible
void processA() {
while( 1 ) {
produce(&data)
send(B, &data);
/* region 1 */
receive(B, &data);
consume(&data);
}
}
void processB() {
while( 1 ) {
receive(A, &data);
transform(&data)
send(A, &data);
/* region 2 */
}
}

## Slide 33: Back to Shared Memory: Mutual Exclusion
Certain sections of code should not be performed concurrently
  Critical section
    Possibly noncontiguous section of code where simultaneous updates, by multiple processes to a shared memory location, can occur
When a process enters the critical section, all other processes must be locked out until it leaves the critical section
  Mutex
    A shared object used for locking and unlocking segment of shared data
    Disallows read/write access to memory it guards
    Multiple processes can perform lock operation simultaneously, but only one process will acquire lock
    All other processes trying to obtain lock will be put in blocked state until unlock operation performed by acquiring process when it exits critical section
    These processes will then be placed in runnable state and will compete for lock again

## Slide 34: Correct Shared Memory Solution to the Consumer-Producer Problem
The primitive mutex is used to ensure critical sections are executed in mutual exclusion of each other
Following the same execution sequence as before:
  A/B execute lock operation on count_mutex
  Either A or B will acquire lock
    Say B acquires it
    A will be put in blocked state
  B loads count (count = 3) from memory into register R2 (R2 = 3)
  B decrements R2 (R2 = 2)
  B stores R2 back to count in memory (count = 2)
  B executes unlock operation
    A is placed in runnable state again
  A loads count (count = 2) from memory into register R1 (R1 = 2)
  A increments R1 (R1 = 3)
  A stores R1 back to count in memory (count = 3)
Count now has correct value of 3
01: data_type buffer[N];
02: int count = 0;
03: mutex count_mutex;
04: void processA() {
05: int i;
06: while( 1 ) {
07: produce(&data);
08: while( count == N );/*loop*/
09: buffer[i] = data;
10: i = (i + 1) % N;
11: count_mutex.lock();
12: count = count + 1;
13: count_mutex.unlock();
14: }
15: }
16: void processB() {
17: int i;
18: while( 1 ) {
19: while( count == 0 );/*loop*/
20: data = buffer[i];
21: i = (i + 1) % N;
22: count_mutex.lock();
23: count = count - 1;
24: count_mutex.unlock();
25: consume(&data);
26: }
27: }
28: void main() {
29: create_process(processA);
30: create_process(processB);
31: }

## Slide 35: Process Communication
Try modeling “req” value of our elevator controller
  Using shared memory
  Using shared memory and mutexes
  Using message passing
buttons
inside
elevator
Unit
Control
b1
down
open
floor
...
Request
Resolver
...
up/down
buttons on each
floor
b2
bN
up1
up2
dn2
dnN
req
up
System interface
up3
dn3

## Slide 36: A Common Problem in Concurrent Programming: Deadlock
Deadlock: A condition where 2 or more processes are blocked waiting for the other to unlock critical sections of code
  Both processes are then in blocked state
  Cannot execute unlock operation so will wait forever
Example code has 2 different critical sections of code that can be accessed simultaneously
  2 locks needed (mutex1, mutex2)
  Following execution sequence produces deadlock
    A executes lock operation on mutex1 (and acquires it)
    B executes lock operation on mutex2( and acquires it)
    A/B both execute in critical sections 1 and 2, respectively
    A executes lock operation on mutex2
      A blocked until B unlocks mutex2
    B executes lock operation on mutex1
      B blocked until A unlocks mutex1
    DEADLOCK!
One deadlock elimination protocol requires locking of numbered mutexes in increasing order and two-phase locking (2PL)
  Acquire locks in 1st phase only, release locks in 2nd phase
01: mutex mutex1, mutex2;
02: void processA() {
03: while( 1 ) {
04: …
05: mutex1.lock();
06: /* critical section 1 */
07: mutex2.lock();
08: /* critical section 2 */
09: mutex2.unlock();
10: /* critical section 1 */
11: mutex1.unlock();
12: }
13: }
14: void processB() {
15: while( 1 ) {
16: …
17: mutex2.lock();
18: /* critical section 2 */
19: mutex1.lock();
20: /* critical section 1 */
21: mutex1.unlock();
22: /* critical section 2 */
23: mutex2.unlock();
24: }
25: }

## Slide 37: Synchronization among processes
Sometimes concurrently running processes must synchronize their execution
  When a process must wait for:
    another process to compute some value
    reach a known point in their execution
    signal some condition
Recall producer-consumer problem
  processA must wait if buffer is full
  processB must wait if buffer is empty
  This is called busy-waiting
    Process executing loops instead of being blocked
    CPU time wasted
More efficient methods
  Join operation, and blocking send and receive discussed earlier
    Both block the process so it doesn’t waste CPU time
  Condition variables and monitors

## Slide 38: Condition variables
Condition variable is an object that has 2 operations, signal and wait
When process performs a wait on a condition variable, the process is blocked until another process performs a signal on the same condition variable
How is this done?
  Process A acquires lock on a mutex
  Process A performs wait, passing this mutex
    Causes mutex to be unlocked
  Process B can now acquire lock on same mutex
  Process B enters critical section
    Computes some value and/or make condition true
  Process B performs signal when condition true
    Causes process A to implicitly reacquire mutex lock
    Process A becomes runnable

## Slide 39: Condition variable example: consumer-producer
2 condition variables
  buffer_empty
    Signals at least 1 free location available in buffer
  buffer_full
    Signals at least 1 valid data item in buffer
processA:
  produces data item
  acquires lock (cs_mutex) for critical section
  checks value of count
  if count = N, buffer is full
    performs wait operation on buffer_empty
    this releases the lock on cs_mutex allowing processB to enter critical section, consume data item and free location in buffer
    processB then performs signal
  if count < N, buffer is not full
    processA inserts data into buffer
    increments count
    signals processB making it runnable if it has performed a wait operation on buffer_full
01: data_type buffer[N];
02: int count = 0;
03: mutex cs_mutex;
04: condition buffer_empty, buffer_full;
06: void processA() {
07: int i;
08: while( 1 ) {
09: produce(&data);
10: cs_mutex.lock();
11: if( count == N ) buffer_empty.wait(cs_mutex);
13: buffer[i] = data;
14: i = (i + 1) % N;
15: count = count + 1;
16: cs_mutex.unlock();
17: buffer_full.signal();
18: }
19: }
20: void processB() {
21: int i;
22: while( 1 ) {
23: cs_mutex.lock();
24: if( count == 0 ) buffer_full.wait(cs_mutex);
26: data = buffer[i];
27: i = (i + 1) % N;
28: count = count - 1;
29: cs_mutex.unlock();
30: buffer_empty.signal();
31: consume(&data);
32: }
33: }
34: void main() {
35: create_process(processA); create_process(processB);
37: }
Consumer-producer using condition variables

## Slide 40: Monitors
Collection of data and methods or subroutines that operate on data similar to an object-oriented paradigm
Monitor guarantees only 1 process can execute inside monitor at a time
(a) Process X executes while Process Y has to wait
(b) Process X performs wait on a condition
  Process Y allowed to enter and execute
(c) Process Y signals condition Process X waiting on
  Process Y blocked
  Process X allowed to continue executing
(d) Process X finishes executing in monitor or waits on a condition again
  Process Y made runnable again
Process X
Monitor
DATA
CODE
(a)
Process Y
Process X
Monitor
DATA
CODE
(b)
Process Y
Process X
Monitor
DATA
CODE
(c)
Process Y
Process X
Monitor
DATA
CODE
(d)
Process Y
Waiting
Waiting

## Slide 41: Monitor example: consumer-producer
Single monitor encapsulates both processes along with buffer and count
One process will be allowed to begin executing first
If processB allowed to execute first
  Will execute until it finds count = 0
  Will perform wait on buffer_full condition variable
  processA now allowed to enter monitor and execute
  processA produces data item
  finds count < N so writes to buffer and increments count
  processA performs signal on buffer_full condition variable
  processA blocked
  processB reenters monitor and continues execution, consumes data, etc.
01: Monitor {
02: data_type buffer[N];
03: int count = 0;
04: condition buffer_full, condition buffer_empty;
06: void processA() {
07: int i;
08: while( 1 ) {
09: produce(&data);
10: if( count == N ) buffer_empty.wait();
12: buffer[i] = data;
13: i = (i + 1) % N;
14: count = count + 1;
15: buffer_full.signal();
16: }
17: }
18: void processB() {
19: int i;
20: while( 1 ) {
21: if( count == 0 ) buffer_full.wait();
23: data = buffer[i];
24: i = (i + 1) % N;
25: count = count - 1;
26: buffer_empty.signal();
27: consume(&data);
28: buffer_full.signal();
29: }
30: }
31: } /* end monitor */
32: void main() {
33: create_process(processA); create_process(processB);
35: }

## Slide 42: Implementation
Mapping of system’s functionality onto hardware processors:
  captured using computational model(s)
  written in some language(s)
Implementation choice independent from language(s) choice
Implementation choice based on power, size, performance, timing and cost requirements
Final implementation tested for feasibility
  Also serves as blueprint/prototype for mass manufacturing of final product
The choice of computational model(s) is based on whether it allows the designer to describe the system.
The choice of language(s) is based on whether it captures the computational model(s) used by the designer.
The choice of implementation is based on whether it meets power, size, performance and cost requirements.
Sequent.
program
State
machine
Data-
flow
Concurrent processes
C/C++
Pascal
Java
VHDL
Implementation A
Implementation B
Implementation C

## Slide 43: Concurrent process model: implementation
Can use single and/or general-purpose processors
(a) Multiple processors, each executing one process
  True multitasking (parallel processing)
  General-purpose processors
    Use programming language like C and compile to instructions of processor
    Expensive and in most cases not necessary
  Custom single-purpose processors
    More common
(b) One general-purpose processor running all processes
  Most processes don’t use 100% of processor time
  Can share processor time and still achieve necessary execution rates
(c) Combination of (a) and (b)
  Multiple processes run on one general-purpose processor while one or more processes run on own single_purpose processor
Process1
Process2
Process3
Process4
Processor A
Processor B
Processor C
Processor D
Communication Bus
(a)
(b)
Process1
Process2
Process3
Process4
General Purpose Processor
Process1
Process2
Process3
Process4
Processor A
General Purpose Processor
Communication Bus
(c)

## Slide 44: Implementation: multiple processes sharing single processor
Can manually rewrite processes as a single sequential program
  Ok for simple examples, but extremely difficult for complex examples
  Automated techniques have evolved but not common
  E.g., simple Hello World concurrent program from before would look like:
    I = 1; T = 0;
    while (1) {
    Delay(I); T = T + 1;
    if X modulo T is 0 then call PrintHelloWorld
    if Y modulo T is 0 then call PrintHowAreYou
    }
Can use multitasking operating system
  Much more common
  Operating system schedules processes, allocates storage, and interfaces to peripherals, etc.
  Real-time operating system (RTOS) can guarantee execution rate constraints are met
  Describe concurrent processes with languages having built-in processes (Java, Ada, etc.) or a sequential programming language with library support for concurrent processes (C, C++, etc. using POSIX threads for example)
Can convert processes to sequential program with process scheduling right in code
  Less overhead (no operating system)
  More complex/harder to maintain

## Slide 45: Processes vs. threads
Different meanings when operating system terminology
Regular processes
  Heavyweight process
  Own virtual address space (stack, data, code)
  System resources (e.g., open files)
Threads
  Lightweight process
  Subprocess within process
  Only program counter, stack, and registers
  Shares address space, system resources with other threads
    Allows quicker communication between threads
  Small compared to heavyweight processes
    Can be created quickly
    Low cost switching between threads

## Slide 46: Implementation: suspending, resuming, and joining
Multiple processes mapped to single-purpose processors
  Built into processor’s implementation
  Could be extra input signal that is asserted when process suspended
  Additional logic needed for determining process completion
    Extra output signals indicating process done
Multiple processes mapped to single general-purpose processor
  Built into programming language or special multitasking library like POSIX
  Language or library may rely on operating system to handle

## Slide 47: Implementation: process scheduling
Must meet timing requirements when multiple concurrent processes implemented on single general-purpose processor
  Not true multitasking
Scheduler
  Special process that decides when and for how long each process is executed
  Implemented as preemptive or nonpreemptive scheduler
  Preemptive
    Determines how long a process executes before preempting to allow another process to execute
      Time quantum: predetermined amount of execution time preemptive scheduler allows each process (may be 10 to 100s of milliseconds long)
    Determines which process will be next to run
  Nonpreemptive
    Only determines which process is next after current process finishes execution

## Slide 48: Scheduling: priority
Process with highest priority always selected first by scheduler
  Typically determined statically during creation and dynamically during execution
FIFO
  Runnable processes added to end of FIFO as created or become runnable
  Front process removed from FIFO when time quantum of current process is up or process is blocked
Priority queue
  Runnable processes again added as created or become runnable
  Process with highest priority chosen when new process needed
  If multiple processes with same highest priority value then selects from them using first-come first-served
  Called priority scheduling when nonpreemptive
  Called round-robin when preemptive

## Slide 49: Priority assignment
Period of process
  Repeating time interval the process must complete one execution within
    E.g., period = 100 ms
    Process must execute once every 100 ms
  Usually determined by the description of the system
    E.g., refresh rate of display is 27 times/sec
    Period = 37 ms
Execution deadline
  Amount of time process must be completed by after it has started
    E.g., execution time = 5 ms, deadline = 20 ms, period = 100 ms
    Process must complete execution within 20 ms after it has begun regardless of its period
    Process begins at start of period, runs for 4 ms then is preempted
    Process suspended for 14 ms, then runs for the remaining 1 ms
    Completed within 4 + 14 + 1 = 19 ms which meets deadline of 20 ms
    Without deadline process could be suspended for much longer
Rate monotonic scheduling
  Processes with shorter periods have higher priority
  Typically used when execution deadline = period
Deadline monotonic scheduling
  Processes with shorter deadlines have higher priority
  Typically used when execution deadline < period
Process
A
B
C
D
E
F
Period
25 ms
50 ms
12 ms
100 ms
40 ms
75 ms
Priority
5
3
6
1
4
2
Process
G
H
I
J
K
L
Deadline
17 ms
50 ms
32 ms
10 ms
140 ms
32 ms
Priority
5
2
3
6
1
4
Rate monotonic
Deadline monotonic

## Slide 50: Real-time systems
Systems composed of 2 or more cooperating, concurrent processes with stringent execution time constraints
  E.g., set-top boxes have separate processes that read or decode video and/or sound concurrently and must decode 20 frames/sec for output to appear continuous
  Other examples with stringent time constraints are:
    digital cell phones
    navigation and process control systems
    assembly line monitoring systems
    multimedia and networking systems
    etc.
  Communication and synchronization between processes for these systems is critical
  Therefore, concurrent process model best suited for describing these systems

## Slide 51: Real-time operating systems (RTOS)
Provide mechanisms, primitives, and guidelines for building real-time embedded systems
Windows CE
  Built specifically for embedded systems and appliance market
  Scalable real-time 32-bit platform
  Supports Windows API
  Perfect for systems designed to interface with Internet
  Preemptive priority scheduling with 256 priority levels per process
  Kernel is 400 Kbytes
QNX
  Real-time microkernel surrounded by optional processes (resource managers) that provide POSIX and UNIX compatibility
    Microkernels typically support only the most basic services
    Optional resource managers allow scalability from small ROM-based systems to huge multiprocessor systems connected by various networking and communication technologies
  Preemptive process scheduling using FIFO, round-robin, adaptive, or priority-driven scheduling
  32 priority levels per process
  Microkernel < 10 Kbytes and complies with POSIX real-time standard

## Slide 52: Summary
Computation models are distinct from languages
Sequential program model is popular
  Most common languages like C support it directly
State machine models good for control
  Extensions like HCFSM provide additional power
  PSM combines state machines and sequential programs
Concurrent process model for multi-task systems
  Communication and synchronization methods exist
  Scheduling is critical
Dataflow model good for signal processing