## Slide 1: Parallel Computing
Multiprocessor Systems on Chip:
Adv. Computer Arch. for Embedded Systems
By Jason Agron

## Slide 2: Laboratory Times?
Available lab times…
  Monday, Wednesday-Friday
  8:00 AM to 1:00 PM.
We will post the lab times on the WIKI.

## Slide 3: What is parallel computing?
Parallel Computing (PC) is…
  Computing with multiple, simultaneously-executing resources.
  Usually realized through a computing platform that contains multiple CPUs.
    Often times implemented as…
      Centralized Parallel Computer:
        Multiple CPUs with a local interconnect or bus.
      Distributed Parallel Computer:
        Multiple computers networked together.

## Slide 4: Why Parallel Computing?
You can save time (execution time)!
  Parallel tasks can run concurrently instead of sequentially.
You can solve larger problems!
  More computational resources = solve bigger problems!
It makes sense!
  Many problem domains are naturally parallelizable.
  Example - Control systems for automobiles.
    Many independent tasks that require little communication.
    Serialization of tasks would cause the system to break down.
      What if the engine management system waited to execute while you tuned the radio????

## Slide 5: Typical Systems
Traditionally, parallel computing systems are composed of the following:
  Individual computers with multiple CPUs.
  Networks of computers.
  Combinations of both.

## Slide 6: Parallel Computing Systems on Programmable Chips
Traditionally multiprocessor systems were expensive.
  Every processor was an atomic unit that had to be purchased.
  Bus structure and interconnect was not flexible.
Today…
  Soft-core processors/interconnect can be used.
  Multiprocessor systems can be “built” from a program.
  Buy a single FPGA - but X processors can be instantiated.
    Where X is any number of processors that can fit on the target FPGA.

## Slide 7: Parallel Programming
How does one program a parallel computing system?
  Traditionally, programs are defined serially.
    Step-by-step, one instruction per step.
      No explicitly defined parallelism.
  Parallel programming involves separating independent sections of code into tasks.
    Tasks are capable of running concurrently.
      Granularity of tasks is user-definable.
    GOAL - parallel portions of code can execute concurrently so overall execution time is reduced.

## Slide 8: How to describe parallelism?
Data-level (SIMD)
  Lightweight - programmer/compiler handle this, no OS support needed.
  EXAMPLE = forAll()
Thread/Task-level (MIMD)
  Fairly lightweight - little OS support
  EXAMPLE = thread_create()
Process-level (MIMD)
  Heavyweight - a lot of OS support
  EXAMPLE = fork()

## Slide 9: Serial Programs
Program is decomposed into a series of tasks.
  Tasks can be fine-grained or coarse-grained.
    Tasks are made up of instructions.
  Tasks must be executed sequentially!
    Total execution time = ∑(Execution Time(Task))
    What if tasks are independent?
    Why don’t we execute them in parallel?

## Slide 10: Parallel Programs
Total execution time can be reduced if tasks run in parallel.
Problem:
  User is responsible for defining tasks.
    Dividing a program into tasks.
    What each task must do.
    How each task…
      Communicates.
      Synchronizes.

## Slide 11: Parallel Programming Models
Serial programs can be hard to design and debug.
Parallel programs are even harder
Models are needed so programmers can create and understand parallel programs.
A model is needed that allows:
  A single application to be defined.
  Application to take advantage of parallel computing resources.
  Programmer to reason about how the parallel program will execute, communicate, and synchronize.
  Application to be portable to different architectures and platforms.

## Slide 12: Parallel Programming Paradigms
What is a “Programming Paradigm”?
  AKA Programming Model.
    Defines the abstractions that a programmer can use when defining a solution to a problem.
Parallel programming implies that there are concurrent operations.
  So what are typical concurrency abstractions…
    Tasks:
      Threads
      Processes.
    Communication:
      Shared-Memory.
      Message-Passing.

## Slide 13: Shared-Memory Model
Global address space for all tasks.
  A variable, X, is shared by multiple tasks.
  Synchronization is needed in order to keep data consistent.
  Example - Task A gives Task B some data through X.
    Task B shouldn’t read X until Task A has put valid data in X.
    NOTE: Task B and Task A operate on the exact same piece of data, so their operations must be in synch.
  Synchronization is done with:
      Semaphores.
      Mutexes.
      Condition Variables.

## Slide 14: Message-Passing Model
Tasks have their own address space.
Communication must be done through the passing of messages.
  Copies data from one task to another.
Synchronization is handled automatically for the programmer.
  Example - Task A gives Task B some data.
    Task B listens for a message from Task A.
    Task B then operates on the data once it receives the message from Task A.
    NOTE - After receiving the message Task B and Task A have independent copies of the data.

## Slide 15: Comparing the Models
Shared-Memory (Global address space).
  Inter-task communication is IMPLICIT!
  Every task communicates with shared data.
    Copying of data is not required.
  User is responsible for correctly using synchronization operations.
Message-Passing (Independent address spaces).
  Inter-task communication is EXPLICIT!
  Messages require that data is copied.
    Copying data is slow --> Overhead!
  User is not responsible for synchronization operations, just for sending data to and from tasks.

## Slide 16: Shared-Memory Example
Communicating through shared data.
Protection of critical regions.
  Interference can occur if protection is done incorrectly, b/c tasks are looking at the same data.
Task A
  Mutex_lock(mutex1)
  Do Task A’s Job - Modify data protected by mutex1
  Mutex_unlock(mutex1)
Task B
  Mutex_lock(mutex1)
  Do Task B’s Job - Modify data protected by mutex1
  Mutex_unlock(mutex1)

## Slide 17: Shared-Memory Diagram

## Slide 18: Message-Passing Example
Communication through messages.
Interference cannot occur b/c each task has its own copy of the data.
Task A
  Receive_message(TaskB, dataInput)
  Do Task A’s Job - dataOutput = fA(dataInput)
  Send_message(TaskB, dataOutput)
Task B
  Receive_message(TaskA, dataInput)
  Do Task B’s Job - dataOutput = fB(dataInput)
  Send_message(TaskA, dataOutput)

## Slide 19: Message-Passing Diagram

## Slide 20: Comparing the Models (Again)
Shared-Memory
  The idea of data “ownership” is not explicit.
    (+) Program development is simplified and can be done more quickly.
      Interfaces do not have to be clearly defined.
    (-) Lack of specification (and lack of data locality) may lead to difficult code to manage and maintain.
    (-) May be hard to figure out what the code is actually doing.
  Shared-memory doesn’t require copying.
    (+) Very lightweight = Less Overhead and More Concurrency.
    (-) May be hard to scale - Contention for a single memory.

## Slide 21: Comparing the Models (Again, 2)
Message-Passing
  Passing of data is explicit.
    Interfaces must be clearly defined
      (+) Allows a programmer to reason about which tasks communicate and when
      (+) Provides a specification of communication needs.
      (-) Specifications take time to develop.
  Message-passing requires copying of data.
    (+) Each task “owns” its own copy of the data.
    (+) Scales fairly well.
      Separate memories = Less contention and More concurrency.
    (-) Message-passing may be too “heavyweight” for some apps.

## Slide 22: Which Model Is Better?
Neither model has a significant advantage over the other.
However, implementations can be better than one another.
Implementations of each of the models can use underlying hardware of a different model.
  Shared-memory interface on a machine with distributed memory.
  Message-passing interface on a machine that uses a shared-memory model.

## Slide 23: Using a Programming Model
Most implementations of programming models are in the form of libraries .
  Why? C is popular, but has no support.
  Application Programmer Interfaces (APIs)
    The interface to the functionality of the library.
    Enforces policy while holding mechanisms abstract.
  Allows applications to be portable.
      Hide details of the system from the programmer.
      Just as a HLL and a compiler hide the ISA of a CPU.
      A parallel programming library should hide the…
        Architecture, interconnect, memories, etc.

## Slide 24: Popular Libraries
Shared-Memory
  POSIX Threads (Pthreads)
  OpenMP
Message-Passing
  MPI

## Slide 25: Popular Operating Systems (OSes)
Linux
  “Normal” Linux
  Embedded Linux
  ucLinux
eCos
  Maps POSIX calls to native eCos-Threads.
HybridThreads (Hthreads) - Soon to be popular?
  OS components are implemented in hardware for super low-overhead system services.
  Maps POSIX calls to OS components in HW (SWTI).
  Provides a POSIX-compliant wrapper for computations in hardware (HWTI).

## Slide 26: Threads are Lightweight…

## Slide 27: POSIX Thread API Classes
Thread Management
  Work directly with threads.
  Creating, joining, attributes, etc.
Mutexes
  Used for synchronization.
  Used to “MUTually EXclude” threads.
Condition Variables
  Used for communication between threads that use a common mutex.
  Used for signaling several threads on a user-specified condition.

## Slide 28: References/Sources
Introduction to Parallel Computing (LLNL)
  www.llnl.gov/computing/tutorials/parallel_comp/
POSIX Thread Programming (LLNL)
  www.llnl.gov/computing/tutorials/pthreads/#WhyPthreads